## Slide 1: SDN-based Control and Operation of the IP Ran in 4G and LTE Environments Huaimo Chen, Quintin Zhao – Huawei huaimo.chen@huawei.com quintin.zhao@huawei.com Daniel King – Old Dog Consulting daniel@olddog.co.uk
www.isocore.com/mpls2013

## Slide 2: Problem Space – IP RAN
The IP RAN provides connectivity for IP-based mobile broadband (MBB) from LTE and 4G base stations.
  Traditionally high-speed mobile connections have been copper and MLPPP, then IP (PWE and MPLS).
Ratio of MBB subscribers to total mobile subscribers is expected to grow from 15% in 2011 to nearly 40% in 2016.
  However, it is important to maintain traffic classes and QoS.
MBB market is forecast to grow to $1 trillion by 2016, with the bulk of the growth coming from mobile broadband services.
  China is leading the World in MBB services.
  At the end of 2012 China Mobile 25(1) had deployed more than 500,000 nodes to support MBB services.
1. PTN Market Research 2013 Frost & Sullivan

## Slide 3: Requirements for 4G and LTE - IP RAN
Service requirements
  Service delivery across a variety of access speeds (3G, 4G/LTE and and Wifi)
  Rapid deployment of services
  Current LTE services exceed 20, and can be as fast as 100Mbps
  Cell-site capacity of multiple Gbps
Technical requirements for MBB deployment and operation, include:
  Effective management of large AS topologies
  Reduce internal AS convergence times
  Scalability of the network
  Carrier grade availability and reliability
  Quality of Service (QoS) and Quality of Experience (QoE)
  Network Virtualization and abstraction

## Slide 4: IP RAN Enabling Technologies
Software Defined and Flexible Networks
  Automated service planning, with “plug and play”
  Fast Troubleshooting and Problem Resolution
  Dynamic Deployment Protocols and Rapid Services Launch
    Separate and abstract elements within the network, using both centralized and distributed control planes
  Make the Network programmable
    Automated service deployment and operation
    Scalable and predictable policy enforcement
  Application-based Network Operations (ABNO) architecture.
  Centralized control of network services
  ABNO provides the mechanisms to request and setup new services, using well-defined standards based path computation, provisioning and reservation protocols and procedures
Topology-Transparent Zone (TTZ)
  Deployed for network virtualization, resolving internal AS scalability and convergence
Enhanced MPLS Procedures and Protocol extensions.
  Multi-topology
  Support separation of traffic across low latency (for mobile voice) and high capacity (for mobile data) links

## Slide 5
Planning IP Address
Dividing IGP Area
Planning CSG&AGG ring relations
SDN-based Mobile Backhaul：Free Services Planning
CSG
AGG
AGG
CSG
CSG
Planning IP Address
Dividing IGP Area
Planning CSG&AGG ring relations
Mobile Backhaul： Complex services planning
Saving
Plug and Play，Zero Touch for Basic Network
Main
Backup
Central Controller
Control Agent
Control Agent
Control Agent
 | Current IP RAN Access Solution | Central Controlled IP RAN
IGP | Yes | Automatic deployment
RSVP-TE | Yes | No
Protocol
Solution
IP RAN Enabling Technologies:
Automated Service Planning, Plug and Play

## Slide 6
IP RAN Enabling Technologies:
Dynamic Deployment Protocols and Rapid Services Launch
Mobile Backhaul
Central Controlled IP RAN
Protocol-based point-by-point services launch
Service-based end-to-end services launch
Improves efficiency of services launch
Lowers skill requirements of staff
Simple protocol Automatic configuration
ATM RNC
Last Mile
Access
Aggregation
RNC/SGW/MME
RSG
RSG
BTS
NodeB / eNB
E1
Eth
IP RNC/S-GW/MME
NodeB
ATM
BSC
STM-1
STM-1
GE
AGG
AGG
CSG
CSG
CSG
IGP/LDP/RSVP
IGP/LDP/RSVP
IGP/LDP/RSVP
IGP/LDP/RSVP
IGP/LDP/RSVP
L2VPN
L2VPN
ATM RNC
Last Mile
Access
Aggregation
RNC/SGW/MME
RSG
RSG
BTS
NodeB / eNB
E1
Eth
IP RNC/S-GW/MME
NodeB
ATM
BSC
STM-1
STM-1
GE
CSG
CSG
AGG
AGG
CSG
Control Plane
Control Plane
Control Plane
Main
Backup
Central Controller
Control Agent
Control Agent
Control Agent
Virtual-cluster enable
Configure remote-interface

## Slide 7
ATM RNC
Last Mile
Access
Aggregation
RNC/SGW/MME
RSG
RSG
CSG
BTS
NodeB/eNB
E1
Eth
IP RNC/S-GW/MME
NodeB
ATM
BSC
STM-1
STM-1
GE
AGG
AGG
CSG
CSG
IP RAN Enabling Technologies:
Fast Troubleshooting and Problem Resolution
Mobile Backhaul
SDN-based Mobile Backhaul
ATM RNC
Last Mile
Access
Aggregation
RNC/SGW/MME
RSG
RSG
BTS
NodeB/eNB
E1
Eth
IP RNC/S-GW/MME
NodeB
ATM
BSC
STM-1
STM-1
GE
CSG
CSG
CSG
AGG
AGG
Control Plane
Control Plane
Control Plane
Main
Backup
Central Controller
Control Agent
Control Agent
Control Agent
NMS
NMS
failure
failure
Trouble shooting on each node
Each node sends alarm independently
Trouble shooting only on Central Controller
Alarm analysis for Locating root causes of fault

## Slide 8: IP RAN Enabling Technologies Application-based Network Operations
Framework for centralized control of network services using well-defined technologies
ABNO provides the mechanisms to request and setup new services, using well-defined standards based path computation, provisioning and reservation protocols and procedures
  Well-known northbound and southbound interfaces
    Application: JSON/XML/SOAP, etc.
    Network: PCEP, RSVP-TE, LDP, OSPF, ISIS, etc.
  Deterministic management of services using PCE
    Stateful, stateless, active, P2P/P2MP, concurrent path computation, PCC-initiated, PCE-initiated
OSS / NMS / 4G / LTE Service Orchestrator
ABNO Controller
OAM Handler
Policy Agent
ALTO Server
Databases TED
LSP-DB
Provisioning Manager
Client Network Layer
Server Network Layer
I2RS Client
PCE
VNTM

## Slide 9
Scaling management during the deployment and operation of IP RANs.
  Especially challenging if ASs already exist and are connected
  Need to reduce network configuration and management of LSAs
A group of routers connected by links with Topology-Transparent Zone (TTZ) ID
  Virtualized as a group of TTZ edge routers fully connected or as a single router
  Links, routers inside TTZ are NOT advertised to routers outside of TTZ
R6
R8
R10
R2
R3
T4
T2
T5
T8
T3
T9
T10
T1
T7
T6
TTZ
T4
T3
T10
T1
R6
R8
R10
R2
R11
R3
R5
RT
T4
T2
T5
T8
T3
T9
T10
T1
T7
T6
TTZ
A group of TTZ edge routers
A single router
IP RAN Enabling Technologies Topology-Transparent Zones

## Slide 10: IP RAN Enabling Technologies: Smooth Migration to TTZ
Migration to TTZ with minimum interruption
Configure TTZ: routers in TTZ work as normal and prepare for TTZ
Allow router to TTZ after it is ready for TTZ
Activate TTZ: all routers in TTZ transfer to work as TTZ routers in ms
Page 10
R6
R7
R8
R10
R9
R4
R1
R2
R11
R3
R5
T4
T2
T5
T8
T3
T9
T10
T1
T7
T6
TTZ
Normal links
TTZ link states “viewed” after configure TTZ
(LSA with TTZ TLV or LSA with I bit generated and distributed)
2. Allow it to TTZ after it has a complete TTZ topology as configured
3. Activate TTZ after all routers in TTZ are allowed to TTZ.
(Generate and distribute LSA for virtualizing TTZ.
Transfer to TTZ)
Generate and distribute LSA for virtualizing TTZ after receiving LSA. Transfer to TTZ.
Normal link
TTZ link

## Slide 11: Simple Set up of E2E TE LSP in AS with TTZ
Path for LSP is computed easily in a normal way
LSP can set up along the path computed
R5
R6
R7
R9
R8
R3
R1
R10
R2
R4
RT
T4
T2
T5
T8
T3
T9
T10
T1
T7
T6
TTZ
Source
Destination
Find path from R3 to R6 in a normal way
Find path from T4 to T7 in a normal way

## Slide 12
Proposed a new virtual network ID design where the single network ID is used to across the service and IGP/MPLS/SDN/ domains to identify the virtual topology corresponding to each individual abstract topology based on the physical topology where the each topology is corresponding to an VPN service and topology pair.
CE2 (VPN_Green)
CE1 (VPN_Green)
PE1
P1
P2
PE2
CE1 (VPN_Gold)
CE2 (VPN_Gold)
IP RAN Enabling Technologies: MPLS MT – Network Virtualization

## Slide 13: Summary
The technologies described meet the service and technical requirements for todays and tomorrows IP RAN
Rapid deployment of services with flexibility, automation and required Quality of Service (QoS) and Quality of Experience (QoE)
  SDN Framework and controller (ABNO)
Carrier grade availability and reliability
  Deterministic path computation and traffic engineering via PCE
  Smooth Migration and path protection
Effective scaling of network
  Topology-Transparent Zones
  Internal AS management and rapid convergence
Network Virtualization and segmentation for customer, and application types
  MPLS multi-topology

## Slide 14: Thanks!